备赞水道

- 概况

备赞濑户是从BINGO NADA的东北边到HARIMA NADA的西南部分的主要航道，全长大约37海里，无数小岛和浅滩接连航道的两边，备赞水道以西部分的岛屿被称作SHIWAKU（SHIAKU）SHOTO。

备赞水道的交通是很拥挤的，大量的渔船经常会被相遇。无数的渡轮来回穿梭于两边的港口。许多的渔船不显示他们的灯光或仅仅在你靠近时才显示。在捕渔的季节，整个交通带都会有渔网，渔网将被设在转潮流时和用两个白浮标志水下锚泊的位置，当潮流很强时，这些浮子有时是很难被发现。

- 交通管理中心

2.1备赞濑户交通管理中心提供信息为所有进入，离开或航行在BISAN SETO EAST，UKO EAST，UKO WEST，BISAN SETO NORTH，BISAN SOUTH AND MIZUSHIMA（水岛）内的船舶。

呼叫：BISAN MARTIS（BISAN MARCHISU）

位置：34°18N133°49.43E

电话：+81（0）877 492220  *492221

传真：+81（0）877 491413

TELEX：+72 5825656 BSTASC

网址：WWW。BISANSETO。KSIHO。MLIT。GO。JP

频道：CH13  16；14  22

信息广播：1651   2019KHZ

  - 24小时程序：

- 交通通告

  - 以下船舶应该在进入航道前的一天的中午报告进入通知。

！巨大型船

！！25000总吨及以上载运液化气的船舶

！！！拖带或顶推长的或大的物体的船舶

！！！！10000总吨及以上的船舶

  - 在3000总吨和10000总吨之间的船舶，及长度70米或以上航行水岛航道的船舶，应该在预计进入航道3小时内报告BISAN MARTIS。

  - 3000总吨或以上的船舶，航行水岛航道的长度70米或以上的船舶，当发布进入通告时也将报告如下信息：

！目的港(当去水岛或SAKAIDE KO时也报告泊位的名称)

！！离开港（当离开水岛或SAKAIDE KO时也报告泊位的名称）

！！！是否有引水的安排

- 船舶在进入航道3小时内，在预计时间有10分钟或以上的变化应该报告变化通知。

- 3000总吨及以上，或航行水岛交通线长度70米或以上的船舶，在穿过报告线时，应该向BISAN MARTIS报告如下信息：

！船名

！！穿过报告线的当地时间

！！！报告线的缩写

- 当航行在雷达的服务区时，船舶应该保持VHF16的守听（或2177KHZ守听如果VHF受不到）

- 所有船舶在进入航道前3小时在雷达服务区域内应该保持VHF16的守听。

- 所有船舶被要求报告他们的位置在通过第一报告线时：

  - 船名

  - 通过报告线的时间

  - 报告线的识别

- 报告点：

| Name of reporting line | abbreviation | Description |
| --- | --- | --- |
| W side of bisan seto S traffic route | SW | A line bearing 180°from futaomote shima lt 34°18.07n133°33.27e to the coast of awa shima |
| S side of bisan seto s traffic route | SS | A line joining NE point of awa shima 34°16.8n133°39.44e with the NW point of shami shima34°21.2n133°49.14e |
| N side of mizushima | MN | A line bearing 075°from the summit of futo noji shima34°26.9n133°45.24e |
| W side of mizushima | MW | A line bearing 180°for 2000m from the summit of futo noji shima |
| Eside of mizushima | ME | A line joining nishino saki sig stn34°26.14n133°47.2e with the NW point of hitsuishi shima34°25.5n133°47.7e |
| S side of bisan seto E traffic route | ES | A line bearing 090°from the summit of kosei shima34°22.5n133°51.14e to the coast and a line bearing 238°for 2860m from the same point |
| N side of uko | UN | A line joining the N point of kama shima 34°25.5n133°50.21e with manaita lshi lt bn34°26.83n133°58.16e |
| S side of uko | US | A line joining megi shima triangulation point34°23.15n134°02.45e with the summit of kusi no yama34°21.5n133°58.7e |
| E end of bisan seto east traffic route | EE | A line joining okushi saki34°22.19n134°12.42e to jizo saki34°24.9n134°13.89e |
| N side of bisan seto east traffic route | EN | A line joining reita saki 34°27.59n134°04.83n to tsuno saki34°27.24n134°00.74e |
| S side of bisan seto east traffic route | EY | A line joining the N point of taka shima 34°23.91n134°10.41e to washiya-no-hama34°25.3n134°07.58e |
| S side of bisan seto east traffic route | ET | A line joining the S point of ogi shima34°24.98n134°03.31e to ananokuchi hana(o shima)34°24.89n134°06.32e |

(8)信息广播：（a）每小时的00-15分和30—45分用日语在1651KHZ

（b）每小时的15—30分和45—00分用英语在2019KHZ

（c）航行信息也可通过电话获得+81（0）877 495166（7）

- 交通规则和规定

- 一条船舶航行在北航路应该航行接近偏西的方向。

- 一条船舶航行在南航路应该航行接近偏东的方向。

- 航行在水岛航路的船舶应该保持在航道中心线靠右一侧行驶。

- 一条船，除了！长度在200m或以上的船舶！！从事捕渔或其它作业的船舶外，当航行在水岛航路里时应该保持给航行在北航路的船舶让路。

- 一条从事捕渔或其它作业的船舶应该给航行在北航路的长度大于200m或以上的船舶让路。

- 一条船，除了长度大于200m的船舶，当航行在北航路时，应该给航行在水岛航路大于200m的船舶让路。

- 一条船，除了长度大于200m的船舶，当航行在北航路或南航路时，应该给航行在水岛航路长度大于200m意图进入北或南航路的船舶让路。

- 除了穿越航路，在以下区域航速被限制在12节以下：

！在USHI SHIMA（34°22N133°47E）的东北端划008°和KOSEI SHIMA外航路的东端之间的区域。

！！在USHI SHIMA的东南端划160°和KOSEI SHIMA外航路的东端之间的区域。

！！！整个水岛交通航路。

- 在来岛海峡和水岛交通航路之间油轮的吃水不应该超过11m。

- 长度在200m或以上的油轮在来岛海峡和水岛航路之间应该有一拖轮护航。

- 当能见度很差时，进入航路被限制如下：

！长度大于200m或以上的船舶；总吨在50000或以上载运危险货物的船舶；总吨在25000或以上载运液化气的船舶；从事拖带或顶推很长物体的船舶，当航路中的能见度小于1海里时，禁止进入。

！！从事载运危险货物除了以上的船舶外，当航路中的能见度小于0.5海里时，禁止进入。

- 在水岛的交通控制

一个信号台在YO SHIMA（34°23N133°49E）的西南面和在NISHINO SAKI（34°26N133°47E）上。信号如下：

| By day | At night | Meaning |
| --- | --- | --- |
| Red light flashing every 2 seconds or black cube | Red light flashing every 2 seconds | n-bound vessels between 70m and 200m in lenth,wait outside mizushima traffic route |
| White light flashing every 2 seconds or black cone point up | White light flashing every 2 seconds | S-bound vessels,between 70m and 200m in lenth,wait outside mizushima traffic route |

如果信号台不工作，交通控制将由巡查船执行如下：在MITSUGO SHIMA（34°22N133°49E）以南附近和MIZUSHIMA KO的港界以内航路的东边。

| By day(international code flags) | At night(by flashing light) | Meaning |
| --- | --- | --- |
| 2nd substitude over flag L | RZN | N-bound vessels between 70m and 200m in lenth,wait outside mizushima traffic route |
| 1st substitude over flag L | RZS | S-bound vessels between 70m and 200m in lenth wait outside mizushima traffic route |

Note:晚上的信号可以白天使用。

- 航路指南

- 所需海图和资料

海图图号：BA3605，3606

潮汐表：中版潮汐表第四册

航路指南：NP42B